## Slide 1: Capacity Planning

## Slide 2: Learning Objective
Capacity Planning
Measuring the service facilities Performance
The Variety of Queuing Models
  Model A: (M/M/1)
  Model B: (M/M/S)
  Model C: (M/D/1)
Factors influencing the waiting time
Case: Workforce Management at Sequoia Airlines

## Slide 3
Dave’s
Car Wash
enter
exit
Population of
dirty cars
Arrivals
from the
general
population …
Queue
(waiting line)
Service
facility
Exit the system
Arrivals to the system
Exit the system
In the system
Example: Capacity planning at Car wash facility
Notes: This slide can be used to frame a discussion of capacity.
Points to be made might include:
- capacity definition and measurement is necessary if we are to develop a production schedule
- while a process may have “maximum” capacity, many factors prevent us from achieving that capacity on a continuous basis.
Students should be asked to suggest factors which might prevent one from achieving maximum capacity.

## Slide 4
Situation | Arrivals in Queue | Service Process
Supermarket | Grocery shoppers | Checkout clerks at cash register
Highway toll booth | Automobiles | Collection of tolls at booth
Doctor’s office | Patients | Treatment by doctors and nurses
Telephone company | Callers | Switching equipment to forward calls
Common Queuing Situations
Notes: This slide provides some reasons that capacity is an issue. The following slides guide a discussion of capacity.

## Slide 5: Crowded Queue

## Slide 6
Size of the population
  Unlimited (infinite)
  Limited (finite)
Pattern of arrivals
  Scheduled
  Random, often a Poisson distribution
Arrival Characteristics
Notes: This slide can be used to frame a discussion of capacity.
Points to be made might include:
- capacity definition and measurement is necessary if we are to develop a production schedule
- while a process may have “maximum” capacity, many factors prevent us from achieving that capacity on a continuous basis.
Students should be asked to suggest factors which might prevent one from achieving maximum capacity.

## Slide 7
0.25 –
0.02 –
0.15 –
0.10 –
0.05 –
–
Probability
0
1
2
3
4
5
6
7
8
9
Distribution for  = 2
x
Pattern of Arrival
Notes: This slide can be used to frame a discussion of capacity.
Points to be made might include:
- capacity definition and measurement is necessary if we are to develop a production schedule
- while a process may have “maximum” capacity, many factors prevent us from achieving that capacity on a continuous basis.
Students should be asked to suggest factors which might prevent one from achieving maximum capacity.

## Slide 8
P(x) = for x = 0, 1, 2, 3, 4, …
e-x
x!
where P(x) = probability of x arrivals
x = number of arrivals per unit of time
 = average arrival rate
Poisson Distribution
Notes: This slide can be used to frame a discussion of capacity.
Points to be made might include:
- capacity definition and measurement is necessary if we are to develop a production schedule
- while a process may have “maximum” capacity, many factors prevent us from achieving that capacity on a continuous basis.
Students should be asked to suggest factors which might prevent one from achieving maximum capacity.

## Slide 9
3. Behavior of arrivals
  Wait in the queue and do not switch lines
  Balking or reneging
Arrival Characteristics

## Slide 10
Limited or unlimited queue length
Queue discipline - first-in, first-out is most common
Other priority rules may be used in special circumstances
Waiting-Line Characteristics
Notes: This slide can be used to frame a discussion of capacity.
Points to be made might include:
- capacity definition and measurement is necessary if we are to develop a production schedule
- while a process may have “maximum” capacity, many factors prevent us from achieving that capacity on a continuous basis.
Students should be asked to suggest factors which might prevent one from achieving maximum capacity.

## Slide 11
Queuing system designs
  Single-channel system, multiple-channel system
  Single-phase system, multiphase system
Service Characteristics
Single-channel, single-phase system
Queue
Arrivals
Service facility
dentist’s office
Departures
after service
Notes: This slide can be used to frame a discussion of capacity.
Points to be made might include:
- capacity definition and measurement is necessary if we are to develop a production schedule
- while a process may have “maximum” capacity, many factors prevent us from achieving that capacity on a continuous basis.
Students should be asked to suggest factors which might prevent one from achieving maximum capacity.

## Slide 12
Single-channel, multiphase system
Arrivals
Departures
after service
Phase 1 service facility
Phase 2 service facility
Queue
Passport office
Queuing System Designs
Notes: This slide can be used to frame a discussion of capacity.
Points to be made might include:
- capacity definition and measurement is necessary if we are to develop a production schedule
- while a process may have “maximum” capacity, many factors prevent us from achieving that capacity on a continuous basis.
Students should be asked to suggest factors which might prevent one from achieving maximum capacity.

## Slide 13
Multi-channel, single-phase system
Queuing System Designs
Arrivals
Queue
Airport Security Check-in
Departures
after service
Service facility
Channel 1
Service facility
Channel 2
Service facility
Channel 3
Notes: This slide can be used to frame a discussion of capacity.
Points to be made might include:
- capacity definition and measurement is necessary if we are to develop a production schedule
- while a process may have “maximum” capacity, many factors prevent us from achieving that capacity on a continuous basis.
Students should be asked to suggest factors which might prevent one from achieving maximum capacity.

## Slide 14
Multi-channel, multiphase system
Arrivals
Queue
Baggage drop and Security check
Departures
after service
Phase 2 service facility
Channel 1
Phase 2 service facility
Channel 2
Phase 1 service facility
Channel 1
Phase 1 service facility
Channel 2
Queuing System Designs
Notes: This slide can be used to frame a discussion of capacity.
Points to be made might include:
- capacity definition and measurement is necessary if we are to develop a production schedule
- while a process may have “maximum” capacity, many factors prevent us from achieving that capacity on a continuous basis.
Students should be asked to suggest factors which might prevent one from achieving maximum capacity.

## Slide 15
2. Service time distribution
  Constant service time
  Random service times, usually a negative exponential distribution
Service Characteristics

## Slide 16
Total expected cost
Cost of Capacity
Cost
Low level
of service
High level
of service
Cost of waiting time
Minimum
Total
cost
Optimal
service level
Queuing Costs = Waiting cost + Cost of Capacity
Notes: This slide can be used to frame a discussion of capacity.
Points to be made might include:
- capacity definition and measurement is necessary if we are to develop a production schedule
- while a process may have “maximum” capacity, many factors prevent us from achieving that capacity on a continuous basis.
Students should be asked to suggest factors which might prevent one from achieving maximum capacity.

## Slide 17
Average time that each customer or object spends in the queue
Average queue length
Average time in the system
Average number of customers in the system
Probability the service facility will be idle
Utilization factor for the system
Probability of a specified number of customers in the system
Measuring Queue Performance
Notes: This slide can be used to frame a discussion of capacity.
Points to be made might include:
- capacity definition and measurement is necessary if we are to develop a production schedule
- while a process may have “maximum” capacity, many factors prevent us from achieving that capacity on a continuous basis.
Students should be asked to suggest factors which might prevent one from achieving maximum capacity.

## Slide 18
 = Average number of arrivals per time period
µ = Average number of units served per time period
Lq = Average number of customer in Queue
Ls = Average number of customer in System
Wq = Average waiting time of customer in the queue
Ws = Average waiting time of customer in the system

## Slide 19: Little’s law

µ
Ls = Lq +
Average number of customers in system
Ws = Wq +
1
µ
Average waiting time in system
Ls = *Ws
Average number of customer in System
Lq = *Wq
Average number of customer in Queue

## Slide 20
Arrivals are FIFO and every arrival waits to be served regardless of the length of the queue
Arrivals are independent of preceding arrivals but the average number of arrivals does not change over time
Service times occur according to the negative exponential distribution
The service rate is faster than the arrival rate
Model A - Single Channel
Notes: This slide can be used to frame a discussion of capacity.
Points to be made might include:
- capacity definition and measurement is necessary if we are to develop a production schedule
- while a process may have “maximum” capacity, many factors prevent us from achieving that capacity on a continuous basis.
Students should be asked to suggest factors which might prevent one from achieving maximum capacity.

## Slide 21
Ls = Average number of units (customers) in the system (waiting and being served)
=
p = Utilization factor for the system
=

µ – 
Model A - Single Channel

µ
Notes: This slide can be used to frame a discussion of capacity.
Points to be made might include:
- capacity definition and measurement is necessary if we are to develop a production schedule
- while a process may have “maximum” capacity, many factors prevent us from achieving that capacity on a continuous basis.
Students should be asked to suggest factors which might prevent one from achieving maximum capacity.

## Slide 22
P0 = Probability of 0 units in the system (that is, the service unit is idle)
= 1 –
Pn > k = Probability of more than k units in the system, where n is the number of units in the system

µ

µ
k + 1
Model A - Single Channel
Notes: This slide can be used to frame a discussion of capacity.
Points to be made might include:
- capacity definition and measurement is necessary if we are to develop a production schedule
- while a process may have “maximum” capacity, many factors prevent us from achieving that capacity on a continuous basis.
Students should be asked to suggest factors which might prevent one from achieving maximum capacity.

## Slide 23
Tom Jones, the mechanic at Golden Shop, is able to repair new phones at an average rate of 3 per hour (or about 1 every 20 minutes), according to a negative exponential distribution. Customers seeking this service arrive at the shop on the average of 2 per hour, following a Poisson distribution. They are served on a first-in, first-out basis and come from a very large (almost infinite) population of possible buyers.
Find?
Average customer time in the queue, Average queue length
Average time in the system, Average customers in the system
Probability the service facility will be idle
Utilization factor for the system
Single Channel Example

## Slide 24
 = 2 customer arriving/hour µ= 3 phone serviced/hour
Ls = = = 2 customer in the system on average
Ws = = = 1 hour average waiting time in the system
Lq = = = 1.33 customer waiting in line
2
µ(µ – )

µ – 
1
µ – 
2
3 - 2
1
3 - 2
22
3(3 - 2)
Single Channel Example
Notes: This slide can be used to frame a discussion of capacity.
Points to be made might include:
- capacity definition and measurement is necessary if we are to develop a production schedule
- while a process may have “maximum” capacity, many factors prevent us from achieving that capacity on a continuous basis.
Students should be asked to suggest factors which might prevent one from achieving maximum capacity.

## Slide 25
Wq = = = 40 minute average waiting time
p = /µ = 2/3 = 66.6% of time mechanic is busy

µ(µ – )
2
3(3 - 2)

µ
P0 = 1 - = .33 probability there are 0 customers in the system
 = 2 customer arriving/hour µ= 3 phone serviced/hour
Single Channel Example
Notes: This slide can be used to frame a discussion of capacity.
Points to be made might include:
- capacity definition and measurement is necessary if we are to develop a production schedule
- while a process may have “maximum” capacity, many factors prevent us from achieving that capacity on a continuous basis.
Students should be asked to suggest factors which might prevent one from achieving maximum capacity.

## Slide 26
M = number of channels open
 = average arrival rate
µ = average service rate at each channel
P0 = for Mµ > 
1
1
M!
1
n!
Mµ
Mµ - 
M – 1
n = 0

µ
n

µ
M
+
∑
Ls = P0 +
µ(/µ)
M
(M - 1)!(Mµ - )
2

µ
Multi-Channel Model
Notes: This slide can be used to frame a discussion of capacity.
Points to be made might include:
- capacity definition and measurement is necessary if we are to develop a production schedule
- while a process may have “maximum” capacity, many factors prevent us from achieving that capacity on a continuous basis.
Students should be asked to suggest factors which might prevent one from achieving maximum capacity.

## Slide 27
 | Single Channel | Two Channels
 | 0.67 | 0.5
P0 | .33 | .5
Ls | 2 customer | .75 customer
Ws | 60 minutes | 22.5 minutes
Lq | 1.33 customer | .083 customer
Wq | 40 minutes | 2.5 minutes
Multi-Channel Example

µ
Notes: This slide can be used to frame a discussion of capacity.
Points to be made might include:
- capacity definition and measurement is necessary if we are to develop a production schedule
- while a process may have “maximum” capacity, many factors prevent us from achieving that capacity on a continuous basis.
Students should be asked to suggest factors which might prevent one from achieving maximum capacity.

## Slide 29
Lq =
2
2µ(µ – )
Average length of queue
Wq =

2µ(µ – )
Average waiting time in queue
Constant Service Model
Notes: This slide can be used to frame a discussion of capacity.
Points to be made might include:
- capacity definition and measurement is necessary if we are to develop a production schedule
- while a process may have “maximum” capacity, many factors prevent us from achieving that capacity on a continuous basis.
Students should be asked to suggest factors which might prevent one from achieving maximum capacity.

## Slide 30: Example
Trucks arrive at a warehouse at a rate of 15 per hour during business hours. Crews can unload the trucks at a rate of 5 per hour. The high unloading rate is due to cargo being containerized. Recent changes in wage rates have caused the warehouse manager to reexamine the question of how many crews to use. The new rates are:
  crew and dock is $100 per hour
  truck and driver cost is $120 per hour
# of Crews | Crews & Dock Cost | Avg. # of trucks in System | Driver/ Truck cost | Total Cost
4 | 400 | 1.528 + 3 = 4.528 | 543.36 | = 943.6
5 | 500 | 0.354 + 3 = 3.354 | 402.48 | = 902.48
6 | 600 | 0.099 + 3 = 3.099 | 371.88 | = 971.88
7 | 700 | 0.028 + 3 = 3.028 | 363.36 | =1063.36

## Slide 31: Psychology of waiting time
Occupied time feels shorter than unoccupied time
Uncertain waits are longer than known
Unexplained waits are longer than explained waits
Unfair waits are longer than equitable waits
The more valuable are the services, the longer the customers wait
Solo waits feels longer than groups

## Slide 32: Alternative solutions
Companies have come up with some novel solutions:
Charging customers for skipping or advancing in the line.
Use distraction: Reading materials, television or conversation.
Keep customers informed
Inform overestimated waiting time to customers

## Slide 33: Tips/tricks for customer
Choose left side for faster service (Robert Samuel, founder of Same Ole Line Dudes)
Look for female cashiers (Prof. Marsden, Beacon College, Leesburg)
Study the customers ahead (Prof. Marsden, Beacon College, Leesburg)
Beware of lines with obstructions (Prof. Niederhoff , University of Washington)
Choose a single line that leads to several cashiers (Julie Niederhoff, Syracuse University)
The variance is larger for the parallel line system than for the single serpentine line- meaning that you could be served very quickly, or have a very long delay (Prof. Richard Larson, MIT)

## Slide 34
Sequoia Airlines Case

## Slide 35: Sequoia Airlines
Sequoia Airlines is a well-established regional airline serving
  California,
  Nevada,
  Arizona,
  Utah.
Sequoia competes on the basis of:
  Price,
  Frequency of flight service,
  Ability to meet schedules,
  Baggage handling,
  Service delivery through flight attendants

## Slide 36: Sequoia Airlines
Maintaining its flight-attendant staff at desired levels has been difficult in the past, however, and many times, it has had to ask flight attendants to work overtime because of worker shortages.
This has resulted in:
  Excessive personnel costs
  Morale problems among the attendants.
  Turnover rate is higher-than-industry-average
  Experienced attendants being hired away by competitors

## Slide 37
Data analysis was performed on the 6-month data of flight attendants hiring and firing for the upcoming time period.
Sequoia Airlines
Month | Demand (attendant hours)
July | 14000
August | 16000
September | 13000
October | 12000
November | 18000
December | 20000

## Slide 38
Sequoia’s training program for new personnel requires an entire month of classroom preparation before they are assigned to regular flight service. As junior flight attendants, they remain on probationary status for 1 additional month.
Sequoia Airlines

## Slide 39
During the training period, each new employee is paid $750.
Junior flight attendant works an average of 140 hours per month and is paid a salary of $1,050 during the probationary period.
Experienced flight attendants works an average of 125 hours per month and is paid a salary of $1,400 per month.
Each instructor receives a salary of $1,500 per month.
Sequoia Airlines

## Slide 40
There are at most 5 trainees per instructor.
Instructors not needed in a particular month (i.e., surplus) may be used as flight attendants.
The proportion of junior flight attendant hours not exceed 25 percent of any month’s total (i.e., junior plus experienced) attendant hours.
In May, Sequoia hired 10 new employees to enter the training program,
In June, it hired 10 more.
At the beginning of June, there were 120 experienced flight attendants and 6 instructors on Sequoia’s staff.
Sequoia Airlines

## Slide 41
For the forecast period (i.e., July–December), determine the number of new trainees who must be hired at the beginning of each month so that total personnel costs for the flight-attendant staff and training program are minimized?
Formulate the problem as an LP model and solve?
How would you deal with non-integer results?
Discuss how you would use the LP model to make your hiring decision for the next six months?
Sequoia Airlines

## Slide 42
Solution
Minimize:

## Slide 43
Solution
Subject to:
+ ≥ , for all i = 1, 2,…6
), for all i = 1, 2,…6
≥ , for all i = 1, 2,…6
= , for all i = 2, 3,…6
= , for all i = 2, 3,…6
= , for all i = 2, 3,…6
= , for all i = 1, 2,…6
=
=
=
≥ 0, ≥ 0, ≥ 0, for all i = 1, 2,…6

## Slide 44
Thank You