## Slide 1: Operations Management with Six Sigma
Dr. Gopal Kumar
gopalkumar@iimraipur.ac.in
IIM Raipur
09 February 2020

## Slide 2: Process Capability
Process capability is ability of a process producing conformance to the specification.
It is a measure of the relationship between the natural variation of the process and the design specifications
  Where is the process centered?
  How much variability exists in the process?
  Is the performance relative to specifications acceptable?
  What proportion of output will be expected to meet specifications?
  What factors contribute to variability?

## Slide 3: Process Capability

## Slide 4: Process Capability
Approximately normal distribution

## Slide 5: Process Capability
LSL
USL
UL
LL
Tolerance
Process variation
LSL
USL
UL
LL
Tolerance
Process variation
Process is capable
(Process variation < Tolerance)
Process is not capable
(Process variation > Tolerance)

## Slide 6: Process Capability
If lower specification limit is 10.55 and upper specification limit is 10.90, the process will produce some non-conforming units.
LSL=10.55
USL=10.90
LL=10.456
UL=10.90
Process is not capable
(Process variation > Tolerance)
The process is producing some defective units, i.e., non-conformance
to the specification.

## Slide 7: Process Capability
Area below the lower specification (10.55)
= NORM.DIST(10.55, 10.7171, 0.0868, TRUE) = 0.0271
Area above the upper specification (10.90)
=1- NORM.DIST(10.90, 10.7171, 0.0868, TRUE)= 0.0176
Process output
Mean () = 10.7171
Standard deviation (s) = 0.0868
Probability that output or a part will not meet specification
= 0.0271 + 0.0176 = 0.0447 OR 4.47%

## Slide 8: Process Capability
Not
capable
Capable
Capable

## Slide 9: Process Capability
Process capability is a measure of the relationship between the natural variation of the process and the design specifications
A capable process must have a Cp of at least 1.0
Six Sigma quality requires a Cp = 2.0
Cp =
Upper Specification – Lower Specification
6s

## Slide 10: Process Capability
Axles production:
Cp =
Upper Specification - Lower Specification
6s
Process mean x = 25 cm
Process standard deviation s = 0.005 cm
Design specification = 25 ± 0.02 cm
25.02 – 24.98
6(0.005)
= 1.33
=
Process is capable

## Slide 11: Process Capability Index
Axles production:
When process mean is not at the center of the specification:
A capable process is not necessarily in the center of the specification, but it falls within the specification limit at both extremes
A capable process must have a Cpk of at least 1.0

## Slide 12: Process Capability Index
.
Target value for the process mean = 140 degrees
Design specification: USL=148 degrees
LSL=132 degrees
Process mean, = 139.8 degrees
Process standard deviation s = 2.14 degree
= 1.21
Process is capable
Process mean (139.8 degrees)

## Slide 13: Pattern in Control Chart
Controlled Process
No points are outside control limits.
The number of points above and below the center line is about the same.
The points seem to fall randomly above and below the center line.
Most points, but not all, are near the center line, and only a few are close to the control limits.

## Slide 14: Pattern in Control Chart
Out-of-Control Pattern
Sudden shift in process average
Cycles
Trends
Hugging the center line
Hugging the control limits

## Slide 15: Pattern in Control Chart
Out-of-Control Pattern
Sudden shift in process average

## Slide 16: Pattern in Control Chart
Out-of-Control Pattern
Sudden shift in process average

## Slide 17: Pattern in Control Chart
Out-of-Control Pattern
Cycles
Possible causes
Operator rotation
Fatigue at the
end of the shift
Different gauges
used by different
inspectors
Seasonal effects

## Slide 18: Pattern in Control Chart
Out-of-Control Pattern
Trends
Possible causes
Improving skills
Improving fatigue
Removing dirt
Changes in temp.
Changes in
humidity
Tool wear

## Slide 19: Pattern in Control Chart
Out-of-Control Pattern
Trends
Possible causes
Improving skills
Improving fatigue
Removing dirt
Changes in temp.
Changes in
humidity
Tool wear
Investigate

## Slide 20: Pattern in Control Chart
Out-of-Control Pattern
Hugging the center line
Possible causes
Miscalculation of
control limit
Wrong placement
of decimal point
Each sample
includes a mixture
of data from two
or more different
Processes.

## Slide 21: Pattern in Control Chart
Out-of-Control Pattern
Hugging the control limits
Possible causes
Each sample is
taken from different
process (but not
mixed together)
and plotted on
the same chart.

## Slide 22: Statistical Process Control Chart
7 Quality Tools
Uses statistics and control charts to tell when to take corrective action
Upper control limit
Coach’s target value
Lower control limit
Game number
| | | | | | | | |
1 2 3 4 5 6 7 8 9
40%
20%
0%
Plot the percent of free throws missed

## Slide 23: Statistical Process Control Chart
7 Quality Tools
Sampling
The purpose of sampling is to find when the process has changed in some nonrandom way, so that the reason for the change can be quickly determined.
Pile of smartphone
A sample of smartphone

## Slide 24: Control Charts for Variables
7 Quality Tools (SPC)
Population and sample

## Slide 25: Control Charts for Variables
7 Quality Tools (SPC)
Population and sample

## Slide 26: Statistical Process Control Chart
7 Quality Tools
Sample testing
Acceptable

## Slide 27: Statistical Process Control Chart
7 Quality Tools
Sampling
Investigate

## Slide 28: Control Charts for Variables
7 Quality Tools (SPC)
.
x-chart tracks changes in the central tendency
R-chart indicates a gain or loss of dispersion

## Slide 29: Control Charts for Variables
7 Quality Tools (SPC)
Central Limit Theorem
If m is the population mean and s is population standard deviation. Then,
The mean of the sampling distribution =
The standard deviation of the sampling distribution =
Where n is the sample size
n=6

## Slide 30: Control Charts for Variables
7 Quality Tools (SPC)
.
For x-Charts when s is known
Where = mean of the sample means or a target value set for the process
z = number of normal standard deviations
= standard deviation of the sample means
s = population (process) standard deviation
n = sample size
Notes: A histogram is a pictorial representation of a set of data. It is created by grouping the measurements into ‘‘cells.’’ Histograms are used to determine the shape of a data set.

## Slide 31: Control Charts for Variables
Population std. dev., σ = 1
7 Quality Tools (SPC)
Example
Sample 1
1 2 3 4 5 6 7 8 9
A sample of size 9
Usually 25 to 30 samples of size 3 to 10 are used.

## Slide 32: Control Charts for Variables
Population std. dev., σ = 1
7 Quality Tools (SPC)
Example
Sample 1
1 2 3 4 5 6 7 8 9
Average weight in the first sample
WEIGHT OF SAMPLE |  | WEIGHT OF SAMPLE |  | WEIGHT OF SAMPLE | 
HOUR | (AVG. OF 9 BOXES) | HOUR | (AVG. OF 9 BOXES) | HOUR | (AVG. OF 9 BOXES)
1 | 16.1 | 5 | 16.5 | 9 | 16.3
2 | 16.8 | 6 | 16.4 | 10 | 14.8
3 | 15.5 | 7 | 15.2 | 11 | 14.2
4 | 16.5 | 8 | 16.4 | 12 | 17.3

## Slide 33: Control Charts for Variables
Population std. dev., σ = 1
Average mean, = 16
7 Quality Tools (SPC)
Example
WEIGHT OF SAMPLE |  | WEIGHT OF SAMPLE |  | WEIGHT OF SAMPLE | 
HOUR | (AVG. OF 9 BOXES) | HOUR | (AVG. OF 9 BOXES) | HOUR | (AVG. OF 9 BOXES)
1 | 16.1 | 5 | 16.5 | 9 | 16.3
2 | 16.8 | 6 | 16.4 | 10 | 14.8
3 | 15.5 | 7 | 15.2 | 11 | 14.2
4 | 16.5 | 8 | 16.4 | 12 | 17.3
Number
of samples = 12
Notes: A histogram is a pictorial representation of a set of data. It is created by grouping the measurements into ‘‘cells.’’ Histograms are used to determine the shape of a data set.

## Slide 34: Control Charts for Variables
Population std. dev., σ = 1
7 Quality Tools (SPC)
Example
Number
of samples = 12

## Slide 35: Control Charts for Variables
Population std. dev., σ = 1
7 Quality Tools (SPC)
Example
17 = UCL
15 = LCL
16 = Mean
Sample number
| | | | | | | | | | | |
1 2 3 4 5 6 7 8 9 10 11 12
Control Chart for samples of 9 boxes
Variation due to assignable causes
Variation due to assignable causes
Variation due to natural causes
Out of control
Out of control
Notes: A histogram is a pictorial representation of a set of data. It is created by grouping the measurements into ‘‘cells.’’ Histograms are used to determine the shape of a data set.

## Slide 36: Control Charts for Variables
7 Quality Tools (SPC)
For x-Charts when we don't know s
Notes: A histogram is a pictorial representation of a set of data. It is created by grouping the measurements into ‘‘cells.’’ Histograms are used to determine the shape of a data set.

## Slide 37: Control Charts for Variables
7 Quality Tools (SPC)
Example
For x-Charts when we don't know s
Where average range of the samples
A2, D3, and D4 = control chart factor shown in Table
= mean of the sample means
Ri = range for sample i
k = total number of samples
X-chart
R-chart
Notes: A histogram is a pictorial representation of a set of data. It is created by grouping the measurements into ‘‘cells.’’ Histograms are used to determine the shape of a data set.

## Slide 38: Control Charts for Variables
7 Quality Tools (SPC)
Example
 | Factors for Computing Control Chart Limits (3 sigma) |  |  | 
SAMPLE SIZE, n |  | MEAN FACTOR, A2 | UPPER RANGE, D4 | LOWER RANGE, D3
2 |  | 1.880 | 3.268 | 0
3 |  | 1.023 | 2.574 | 0
4 |  | .729 | 2.282 | 0
5 |  | .577 | 2.115 | 0
6 |  | .483 | 2.004 | 0
7 |  | .419 | 1.924 | 0.076
8 |  | .373 | 1.864 | 0.136
9 |  | .337 | 1.816 | 0.184
10 |  | .308 | 1.777 | 0.223
12 |  | .266 | 1.716 | 0.284
For x-Charts when we don't know s
Notes: A histogram is a pictorial representation of a set of data. It is created by grouping the measurements into ‘‘cells.’’ Histograms are used to determine the shape of a data set.

## Slide 39: Control Charts for Variables
7 Quality Tools (SPC)
Example
Oat flakes labeled as "net weight 12 ounces"
Process average = 12 ounces
Sample size = 5
For x-Charts when we don't know s

## Slide 40: Control Charts for Variables
7 Quality Tools (SPC)
Example
SAMPLE | WEIGHT OF LIGHTEST PACKET IN SAMPLE OF n = 5 | WEIGHT OF HEAVIEST PACKET IN SAMPLE OF n = 5
1 | 11.50 | 11.72
2 | 11.97 | 12.00
3 | 11.55 | 12.05
4 | 12.00 | 12.20
5 | 11.95 | 12.00
6 | 10.55 | 10.75
7 | 12.50 | 12.75
8 | 11.00 | 11.25
9 | 10.60 | 11.00
10 | 11.70 | 12.10
Sum |  | 
RANGE
.22
.03
.50
.20
.05
.20
.25
.25
.40
.40
2.5
For x-Charts when we don't know s
Notes: A histogram is a pictorial representation of a set of data. It is created by grouping the measurements into ‘‘cells.’’ Histograms are used to determine the shape of a data set.

## Slide 41: Control Charts for Variables
7 Quality Tools (SPC)
Example
SAMPLE SIZE, n | A2 | D4
2 | 1.880 | 3.268
3 | 1.023 | 2.574
4 | .729 | 2.282
5 | .577 | 2.115
6 | .483 | 2.004
7 | .419 | 1.924
8 | .373 | 1.864
9 | .337 | 1.816
10 | .308 | 1.777
12 | .266 | 1.716
For x-Charts when we don't know s

## Slide 42: Control Charts for Variables
7 Quality Tools (SPC)
Example
UCL = 12.144
Mean = 12
LCL = 11.856
For x-Charts when we don't know s

## Slide 43: Control Charts for Variables
R – Chart
7 Quality Tools (SPC)
Example
= 2.115*0.25 =
= 0.00*0.25
0.52875
=0
UCL = 0.5287
Mean = 0.25
LCL = 0
For x-Charts when we don't know s

## Slide 44
7 Quality Tools (SPC)
Control Chart for Attributes Data
.

## Slide 45: Control Chart for Attributes Data
SPC
A unit of work is nonconforming (defect or error) or not.
If a unit of work may have one or more nonconformances, entire unit becomes nonconformaning.
Attributes chart captures nonconforming as well as number of nonconforming. Sudden shift in process average.
p-charts monitors proportion of nonconforming units
c-charts and u-charts monitor the number of nonconformances per unit

## Slide 46: p-charts (Fraction nonconforming)
SPC
Sample size needs to be large enough
Average
Collect k samples. Let yi represent the number of nonconforming units in sample i, and ni be the size of sample i.
Compute the fraction nonconforming in each sample, pi = yi /ni
Average fraction nonconforming
P-chart with fixed sample size

## Slide 47: p-charts (Fraction nonconforming)
SPC
.
Collect k samples. Let yi represent the number of nonconforming units in sample i, and ni be the size of sample i.
Compute the fraction nonconforming in each sample, pi = yi /ni
Average fraction nonconforming
Compute standard deviation
P-chart with fixed sample size

## Slide 48: p-charts (Fraction nonconforming)
SPC
.
Compute standard deviation
P-chart with fixed sample size

## Slide 49: p-charts (Fraction nonconforming)
SPC
.
Chart: p-chart
Fraction nonconforming | 0.03 | 0.01 | 0 | 0 | 0.02 | 0.05 | 0.03 | 0.06 | 0.01 | 0.04 | 0 | 0.02 | 0.01 | 0.03 | 0.04 | 0.01 | 0.01 | 0.02 | 0.05 | 0.02 | 0.03 | 0.04 | 0.01 | 0 | 0.01
 | 0.022 | 0.022 | 0.022 | 0.022 | 0.022 | 0.022 | 0.022 | 0.022 | 0.022 | 0.022 | 0.022 | 0.022 | 0.022 | 0.022 | 0.022 | 0.022 | 0.022 | 0.022 | 0.022 | 0.022 | 0.022 | 0.022 | 0.022 | 0.022 | 0.022
 | 0.066 | 0.066 | 0.066 | 0.066 | 0.066 | 0.066 | 0.066 | 0.066 | 0.066 | 0.066 | 0.066 | 0.066 | 0.066 | 0.066 | 0.066 | 0.066 | 0.066 | 0.066 | 0.066 | 0.066 | 0.066 | 0.066 | 0.066 | 0.066 | 0.066
 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Decreasing trend represents improvement
Upper trend or value above UCL conveys
need for improvement
P-chart with fixed sample size

## Slide 50: p-charts (Fraction nonconforming)
SPC
.
P-chart with fixed sample size
Sample size = 350

## Slide 51: p-charts (Fraction nonconforming)
SPC
.
P-chart with variable sample size

## Slide 52: p-charts (Fraction nonconforming)
SPC
.
P-chart with variable sample size
Chart: p-chart
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20
CL | 0.09094 | 0.09094 | 0.09094 | 0.09094 | 0.09094 | 0.09094 | 0.09094 | 0.09094 | 0.09094 | 0.09094 | 0.09094 | 0.09094 | 0.09094 | 0.09094 | 0.09094 | 0.09094 | 0.09094 | 0.09094 | 0.09094 | 0.09094
UCL | 0.16463 | 0.15956 | 0.18087 | 0.16903 | 0.18395 | 0.15402 | 0.16 | 0.17068 | 0.17318 | 0.16332 | 0.16384 | 0.15541 | 0.15255 | 0.1585 | 0.16384 | 0.16518 | 0.15419 | 0.15303 | 0.15505 | 0.15913
LCL | 0.017245 | 0.022317 | 0.0010105 | 0.012846 | -0.0020737 | 0.027862 | 0.021879 | 0.011195 | 0.0086968 | 0.018554 | 0.018039 | 0.026468 | 0.029327 | 0.023378 | 0.018039 | 0.016701 | 0.027693 | 0.02885 | 0.026825 | 0.022747
Fraction NC | 0.13139 | 0.12658 | 0.15217 | 0.04918 | 0.12791 | 0.11765 | 0.038462 | 0.076923 | 0.12727 | 0.084507 | 0.057143 | 0.072626 | 0.02551 | 0.092025 | 0.17857 | 0.088889 | 0.086022 | 0.062176 | 0.082873 | 0.1125

## Slide 53: np-charts (Fraction nonconforming)
SPC
.
np-chart with fixed sample size

## Slide 54: np-charts (Fraction nonconforming)
SPC
.
np-chart with fixed sample size
= 1.4668

## Slide 55: np-charts (Fraction nonconforming)
SPC
.
np-chart with fixed sample size

## Slide 56: c-charts for nonconforming
SPC
Collect samples of equal size and count the number of nonconformances
Compute the average number of nonconformances per unit, c-bar
Standard deviation
Control limits

## Slide 57: c-charts for nonconforming
SPC
.

## Slide 58: c-charts for nonconforming
SPC
.

## Slide 59: u-charts for nonconforming
SPC
.
Applies if the samples are of unequal size
Collect samples and count the number of nonconformances
Compute the average number of nonconformances per unit, u-bar
Standard deviation
Control limits

## Slide 60: u-charts for nonconforming
SPC
.

## Slide 61: u-charts for nonconforming
SPC
.

## Slide 62: Six Sigma Implementation
6
Think in terms of key business processes and customer requirements with a clear focus on overall strategic objectives.
Focus on corporate sponsors responsible for championing projects, support team activities, help to overcome resistance to change, and obtain resources.
Emphasize such quantifiable measures as DPMO that can be applied to all parts of an organization: manufacturing, engineering, administrative, software, and so on.
Notes: There is no harm in going from 6 to 7 og 8. In fact airline industry operate at 10 or more for flight take off & landing, but for all practical purposses in an industry where human life is not at risk six sigma is a good enough improvement benchmark. More than that may not be worth the Time, money$$ and effort.

## Slide 63: Six Sigma Implementation
6
Ensure that appropriate metrics are identified early in the process and that they focus on business results, thereby providing incentives and accountability.
Provide extensive training followed by project team deployment to improve profitability, reduce non-value-added activities, and achieve cycle time reduction.
Create highly qualified process improvement experts (“Green Belts,” “Black Belts,” and “Master Black Belts”) who can apply improvement tools and lead teams.
Set stretch objectives for improvement.
Notes: There is no harm in going from 6 to 7 og 8. In fact airline industry operate at 10 or more for flight take off & landing, but for all practical purposses in an industry where human life is not at risk six sigma is a good enough improvement benchmark. More than that may not be worth the Time, money$$ and effort.

## Slide 64: Six Sigma Companies
Six Sigma

## Slide 65: Six Sigma Methodology
Six Sigma
Defines the project’s purpose, scope, and outputs, then identifies the required process information keeping in mind the customer’s definition of quality
Measures the process and collects data
Analyzes the data ensuring repeatability and reproducibility
Improves by modifying or redesigning existing processes and procedures
Controls the new process to make sure performance levels are maintained
DMAIC
DMAIC: Dumb Managers Always Ignore Customers
Create qualified process improvement experts (Black Belts, Green Belts, etc.)
Notes: Cummins India Ltd., Tata Consultancy Services is one such name. TATA Motors, John Deere, Mahindra & Mahindra, KPMG, GenPact, Gabriel Motors, Lear Corporation are few other industry giants that are using Six Sigma methodologies.

## Slide 66: DMAIC Tools and Techniques
Six Sigma
.
Notes: Cummins India Ltd., Tata Consultancy Services is one such name. TATA Motors, John Deere, Mahindra & Mahindra, KPMG, GenPact, Gabriel Motors, Lear Corporation are few other industry giants that are using Six Sigma methodologies.

## Slide 67: References.
Managing for Quality and Performance Excellence, Evans, J.R. and William M. Lindsay, W.M., Cengage Learning, India
The Six Sigma Handbook, Tomas Pyzdek and Paul Keller, Fourth edition, McGraw Hill India.
Total Quality Management, Besterfield et al., Revised third edition, Pearson India
The Management and Control of Quality, J. Evans, and W. Lindsay, Third edition, Cengage Learning

## Slide 68: .
Thanks!