## Slide 1: Operations Management with Six Sigma
Dr. Gopal Kumar
gopalkumar@iimraipur.ac.in
IIM Raipur
08 February 2020

## Slide 2: Quality Measurements
Customer Focus
Defects per million opportunities (DPMO)
It is generally easy to move from 2 or 3 sigma level
to 4 sigma level, but moving beyond that requires
much more effort
Notes: Essentially, they are the “hows” by which the company will respond to the “whats”—the customer requirements that will determine customer satisfaction or delight, often called critical to quality characteristics (CTQs).

## Slide 3: Quality Measurements
Customer Focus
Defects per million opportunities (DPMO)
In manufacturing, fault is called defect, i.e., defect per
million opportunity (DPMO)
In service, fault is called error, i.e., error per million
opportunity (EPMO)
Notes: Essentially, they are the “hows” by which the company will respond to the “whats”—the customer requirements that will determine customer satisfaction or delight, often called critical to quality characteristics (CTQs).

## Slide 4: Error per million opportunities (EPMO)
Customer Focus
Lost baggage on airport
If average bag per customer = 2.3
When 10,000 passengers travelled over one month, 4 lost bags were detected
Opportunity for error = = 23000
Sigma Level =
= 5.0768
Baggage handling system on the airport is operating at
more than 5 sigma level
Notes: Essentially, they are the “hows” by which the company will respond to the “whats”—the customer requirements that will determine customer satisfaction or delight, often called critical to quality characteristics (CTQs).

## Slide 5: Normal Distribution
7 Quality Tools
(68%)
.
(95%)
(99.7%)
68% of the population will lie within 1 standard deviation, 1σ, of the mean
95% of the population will lie within 2 standard deviations, 2σ, of the mean
99.7% of the population will lie within 3 standard deviations, 3σ, of the mean
Area under
the curve is
probability

## Slide 6: Normal Distribution
7 Quality Tools
.

## Slide 7: Normal Distribution
7 Quality Tools
.

## Slide 8: Seven Quality Tools
7 Quality Tools
Tools for Generating Ideas
  Check Sheet
  Scatter Diagram
  Cause-and-Effect Diagram
Tools to Organize the Data
  Pareto Chart
  Flowchart (Process Diagram)
Tools for Identifying Problems
  Histogram
  Statistical Process Control Chart

## Slide 9: Check Sheet
7 Quality Tools
  Check Sheet: An organized method of recording data/defects
////
//
////
4
2
5
////
7
//

## Slide 10: Check Sheet
7 Quality Tools
  Inspecting smartphone
    A: Defect in camera
    B: Defect in display
    C: Defect in audio system
Hour
Defect 1 2 3 4 5 6 7 8
A
B
C
/
/
/
/
/
/
/
/
/
/
/
/
/
/
/
/
/
/
/
/
/
/
/
/
/
/
/
/
/
/

## Slide 11: Scatter Diagram
7 Quality Tools
  Scatter Diagram: A graph of the value of one variable vs. another variable
Absenteeism
Productivity
Absenteeism vs. Productivity
If data points form a tight band, the two variables are closely related.
If data points are scattered, the items are unrelated.
Absenteeism and productivity are inversely related .

## Slide 12: Scatter Diagram
7 Quality Tools
  .
Defect rate vs. overtime hours
Defect rate and overtime hours are positively related.

## Slide 13: Cause-and-Effect Diagram
7 Quality Tools
  .
Cause
Materials
Methods
Manpower
Machinery
Effect
Ishikawa diagram or fish-bone diagram
Causes of any
problem are 4 Ms:
Man
Method
Material
Machine

## Slide 14: Cause-and-Effect Diagram
7 Quality Tools
Ishikawa diagram or fish-bone diagram
Causes: 4 Ms

## Slide 15: Cause-and-Effect Diagram
7 Quality Tools
  Problem: Dissatisfied airline customer
Ishikawa diagram or fish-bone diagram
Causes: 4 Ms

## Slide 16: Pareto Chart
7 Quality Tools
  80% of the problems come from 20% of the causes (machines, raw materials, operators etc.)
General use, to decide where to apply initial
effort for maximum effect.
Pareto charts are
a method of
organizing errors,
problems, or
defects to help
focus on problem
solving efforts.

## Slide 17: Pareto Chart
7 Quality Tools
  An avant-garde clothing manufacturer runs a series of high-profile, risqué ads on a billboard on Highway 101 and regularly collects protest calls from people who are offended by them. The company has no idea how many people in total see the ads, but it has been collecting statistics on the number of phone calls from irate viewers:
  a) Depict this data with a Pareto chart. Also depict the cumulative complaint line.
  b) What percent of the total complaints can be attributed to the most prevalent complaint?

## Slide 18: Pareto Chart
7 Quality Tools
  .

## Slide 19: Flowchart
7 Quality Tools
  Flowchart (Process Diagram): A chart that describes the steps in a process

## Slide 20: Histogram
7 Quality Tools
  Histogram: A distribution showing the frequency of occurrences of a variable
Distribution
Repair time (minutes)
Frequency
5
10
15
20
25
30
35
40
45
50
22
18
18
11
11
7
7
3
3

## Slide 21: Histogram
7 Quality Tools
  Histogram:
Frequency

## Slide 22: Histogram
7 Quality Tools
  Histogram
  Possible causes might be two workers or two suppliers with different quality.

## Slide 23: Statistical Process Control Chart
7 Quality Tools
Uses statistics and control charts to tell when to take corrective action
As per Shewhart and Deming, there are two causes of variations:
  Natural causes or common causes (Usual, historical, quantifiable variation in a system)
  Special causes or assignable causes (unusual, not previously observed, non-quantifiable variation)
Notes: https://www.safaribooksonline.com/library/view/operations-management-an/9781118122679/ch6-sec006.html

## Slide 24: Statistical Process Control Chart
7 Quality Tools
Uses statistics and control charts to tell when to take corrective action
Notes: A histogram is a pictorial representation of a set of data. It is created by grouping the measurements into ‘‘cells.’’ Histograms are used to determine the shape of a data set.

## Slide 25: Statistical Process Control Chart
7 Quality Tools
Uses statistics and control charts to tell when to take corrective action
Weight
Time
Frequency
Prediction
If only natural causes of variation are present, the output of a process forms a distribution that is stable over time and is predictable
Notes: A histogram is a pictorial representation of a set of data. It is created by grouping the measurements into ‘‘cells.’’ Histograms are used to determine the shape of a data set.

## Slide 26: Statistical Process Control Chart
7 Quality Tools
Uses statistics and control charts to tell when to take corrective action
If assignable causes are present, the process output is not stable over time and is not predicable
Weight
Time
Frequency
Prediction
?
?
?
?
?
?
?
?
?
?
?
?
?
?
?
?
?
?
?
Notes: A histogram is a pictorial representation of a set of data. It is created by grouping the measurements into ‘‘cells.’’ Histograms are used to determine the shape of a data set.

## Slide 27: Statistical Process Control Chart
7 Quality Tools
Uses statistics and control charts to tell when to take corrective action
Frequency
(weight, length, speed, etc.)
Size
Lower control limit
Upper control limit
(a) In statistical control and capable of producing within control limits
(b) In statistical control but not capable of producing within control limits
(c) Out of control
Notes: A histogram is a pictorial representation of a set of data. It is created by grouping the measurements into ‘‘cells.’’ Histograms are used to determine the shape of a data set.

## Slide 28: Process Capability
Process capability is ability of a process producing conformance to the specification.
It is a measure of the relationship between the natural variation of the process and the design specifications
  Where is the process centered?
  How much variability exists in the process?
  Is the performance relative to specifications acceptable?
  What proportion of output will be expected to meet specifications?
  What factors contribute to variability?

## Slide 29: Process Capability

## Slide 30: Process Capability
Approximately normal distribution

## Slide 31: Process Capability
If design specifications are between 10.55 and 10.90, the process will produce some non-conforming units.
Area below the lower specification (10.55)
= NORM.DIST(10.55, 10.7171, 0.0868, TRUE)
=0.0271

## Slide 32: Process Capability
If design specifications are between 10.55 and 10.90, the process will produce some non-conforming units.
Area above the upper specification (10.90)
=1- NORM.DIST(10.90, 10.7171, 0.0868, TRUE)
=0.0176

## Slide 33: Process Capability
Probability that output or a part will not meet specification
= 0.0271 + 0.0176 = 0.0447
OR
4.47%

## Slide 34: Process Capability
Not capable

## Slide 35: Process Capability
Process capability is a measure of the relationship between the natural variation of the process and the design specifications
A capable process must have a Cp of at least 1.0
Often a target value of Cp = 1.33 is used to allow for off-center processes
Six Sigma quality requires a Cp = 2.0
Cp =
Upper Specification – Lower Specification
6s

## Slide 36: Process Capability
Axles production:
Cp =
Upper Specification - Lower Specification
6s
Process mean x = 25 cm
Process standard deviation s = 0.005 cm
Design specification = 25 ± 0.02 cm
25.02 – 24.98
6(0.005)
= 1.33
=
Process is capable

## Slide 37: Process Capability Index
Axles production:
A capable process is not necessarily in the center of the specification, but it falls within the specification limit at both extremes
A capable process must have a Cpk of at least 1.0

## Slide 38: Process Capability Index
.
Target value for the process mean = 140 degrees
Process mean x = 139.8 degrees
Process standard deviation s = 2.14 degree
Design specification: USL=148 degrees
LSL=132 degrees
= 1.21
Process is capable

## Slide 39: Pattern in Control Chart
Controlled Process
No points are outside control limits.
The number of points above and below the center line is about the same.
The points seem to fall randomly above and below the center line.
Most points, but not all, are near the center line, and only a few are close to the control limits.

## Slide 40: Pattern in Control Chart
Out-of-Control Pattern
Sudden shift in process average
Cycles
Trends
Hugging the center line
Hugging the control limits

## Slide 41: Pattern in Control Chart
Out-of-Control Pattern
Sudden shift in process average

## Slide 42: Pattern in Control Chart
Out-of-Control Pattern
Sudden shift in process average

## Slide 43: Pattern in Control Chart
Out-of-Control Pattern
Cycles
Possible causes
Operator rotation
Fatigue at the
end of the shift
Different gauges
used by different
inspectors
Seasonal effects

## Slide 44: Pattern in Control Chart
Out-of-Control Pattern
Trends
Possible causes
Improving skills
Improving fatigue
Removing dirt
Changes in temp.
Changes in
humidity
Tool wear

## Slide 45: Pattern in Control Chart
Out-of-Control Pattern
Trends
Possible causes
Improving skills
Improving fatigue
Removing dirt
Changes in temp.
Changes in
humidity
Tool wear
Investigate

## Slide 46: Pattern in Control Chart
Out-of-Control Pattern
Hugging the center line
Possible causes
Miscalculation of
control limit
Wrong placement
of decimal point

## Slide 47: Pattern in Control Chart
Out-of-Control Pattern
Hugging the control limits
Possible causes
Miscalculation of
control limit
Wrong placement
of decimal point

## Slide 48: Statistical Process Control Chart
7 Quality Tools
Uses statistics and control charts to tell when to take corrective action
Upper control limit
Coach’s target value
Lower control limit
Game number
| | | | | | | | |
1 2 3 4 5 6 7 8 9
40%
20%
0%
Plot the percent of free throws missed

## Slide 49: Statistical Process Control Chart
7 Quality Tools
Sampling
The purpose of sampling is to find when the process has changed in some nonrandom way, so that the reason for the change can be quickly determined.
Acceptable

## Slide 50: Statistical Process Control Chart
7 Quality Tools
Sampling
Investigate

## Slide 51: Control Charts for Variables
7 Quality Tools (SPC)
.
x-chart tracks changes in the central tendency
R-chart indicates a gain or loss of dispersion

## Slide 52: Control Charts for Variables
7 Quality Tools (SPC)
Population and sample

## Slide 53: Control Charts for Variables
7 Quality Tools (SPC)
Population and sample

## Slide 54: Control Charts for Variables
7 Quality Tools (SPC)
Central Limit Theorem
If m is the population mean and s is population standard deviation. Then,
The mean of the sampling distribution =
The standard deviation of the sampling distribution =

## Slide 55: Control Charts for Variables
7 Quality Tools (SPC)
.
For x-Charts when s is known
Where = mean of the sample means or a target value set for the process
z = number of normal standard deviations
= standard deviation of the sample means
s = population (process) standard deviation
n = sample size
Notes: A histogram is a pictorial representation of a set of data. It is created by grouping the measurements into ‘‘cells.’’ Histograms are used to determine the shape of a data set.

## Slide 56: Control Charts for Variables
Population std. dev., σ = 1
7 Quality Tools (SPC)
Example
Sample 1
1 2 3 4 5 6 7 8 9
A sample of size 9
Usually 25 to 30 samples of size 3 to 10 are used.

## Slide 57: Control Charts for Variables
Population std. dev., σ = 1
7 Quality Tools (SPC)
Example
Sample 1
1 2 3 4 5 6 7 8 9
Average weight in the first sample
WEIGHT OF SAMPLE |  | WEIGHT OF SAMPLE |  | WEIGHT OF SAMPLE | 
HOUR | (AVG. OF 9 BOXES) | HOUR | (AVG. OF 9 BOXES) | HOUR | (AVG. OF 9 BOXES)
1 | 16.1 | 5 | 16.5 | 9 | 16.3
2 | 16.8 | 6 | 16.4 | 10 | 14.8
3 | 15.5 | 7 | 15.2 | 11 | 14.2
4 | 16.5 | 8 | 16.4 | 12 | 17.3

## Slide 58: Control Charts for Variables
Population std. dev., σ = 1
Average mean, = 16
7 Quality Tools (SPC)
Example
WEIGHT OF SAMPLE |  | WEIGHT OF SAMPLE |  | WEIGHT OF SAMPLE | 
HOUR | (AVG. OF 9 BOXES) | HOUR | (AVG. OF 9 BOXES) | HOUR | (AVG. OF 9 BOXES)
1 | 16.1 | 5 | 16.5 | 9 | 16.3
2 | 16.8 | 6 | 16.4 | 10 | 14.8
3 | 15.5 | 7 | 15.2 | 11 | 14.2
4 | 16.5 | 8 | 16.4 | 12 | 17.3
Number
of samples = 12
Notes: A histogram is a pictorial representation of a set of data. It is created by grouping the measurements into ‘‘cells.’’ Histograms are used to determine the shape of a data set.

## Slide 59: Control Charts for Variables
Population std. dev., σ = 1
7 Quality Tools (SPC)
Example
Number
of samples = 12

## Slide 60: Control Charts for Variables
Population std. dev., σ = 1
7 Quality Tools (SPC)
Example
17 = UCL
15 = LCL
16 = Mean
Sample number
| | | | | | | | | | | |
1 2 3 4 5 6 7 8 9 10 11 12
Control Chart for samples of 9 boxes
Variation due to assignable causes
Variation due to assignable causes
Variation due to natural causes
Out of control
Out of control
Notes: A histogram is a pictorial representation of a set of data. It is created by grouping the measurements into ‘‘cells.’’ Histograms are used to determine the shape of a data set.

## Slide 61: Control Charts for Variables
7 Quality Tools (SPC)
Example
For x-Charts when we don't know s
Where average range of the samples
A2, D3, and D4 = control chart factor shown in Table
= mean of the sample means
Ri = range for sample i
k = total number of samples
X-chart
R-chart
Notes: A histogram is a pictorial representation of a set of data. It is created by grouping the measurements into ‘‘cells.’’ Histograms are used to determine the shape of a data set.

## Slide 62: Control Charts for Variables
7 Quality Tools (SPC)
Example
 | Factors for Computing Control Chart Limits (3 sigma) |  |  | 
SAMPLE SIZE, n |  | MEAN FACTOR, A2 | UPPER RANGE, D4 | LOWER RANGE, D3
2 |  | 1.880 | 3.268 | 0
3 |  | 1.023 | 2.574 | 0
4 |  | .729 | 2.282 | 0
5 |  | .577 | 2.115 | 0
6 |  | .483 | 2.004 | 0
7 |  | .419 | 1.924 | 0.076
8 |  | .373 | 1.864 | 0.136
9 |  | .337 | 1.816 | 0.184
10 |  | .308 | 1.777 | 0.223
12 |  | .266 | 1.716 | 0.284
For x-Charts when we don't know s
Notes: A histogram is a pictorial representation of a set of data. It is created by grouping the measurements into ‘‘cells.’’ Histograms are used to determine the shape of a data set.

## Slide 63: Control Charts for Variables
7 Quality Tools (SPC)
Example
Oat flakes labeled as "net weight 12 ounces"
Process average = 12 ounces
Sample size = 5
For x-Charts when we don't know s

## Slide 64: Control Charts for Variables
7 Quality Tools (SPC)
Example
SAMPLE | WEIGHT OF LIGHTEST PACKET IN SAMPLE OF n = 5 | WEIGHT OF HEAVIEST PACKET IN SAMPLE OF n = 5
1 | 11.50 | 11.72
2 | 11.97 | 12.00
3 | 11.55 | 12.05
4 | 12.00 | 12.20
5 | 11.95 | 12.00
6 | 10.55 | 10.75
7 | 12.50 | 12.75
8 | 11.00 | 11.25
9 | 10.60 | 11.00
10 | 11.70 | 12.10
Sum |  | 
RANGE
.22
.03
.50
.20
.05
.20
.25
.25
.40
.40
2.5
For x-Charts when we don't know s
Notes: A histogram is a pictorial representation of a set of data. It is created by grouping the measurements into ‘‘cells.’’ Histograms are used to determine the shape of a data set.

## Slide 65: Control Charts for Variables
7 Quality Tools (SPC)
Example
SAMPLE SIZE, n | A2 | D4
2 | 1.880 | 3.268
3 | 1.023 | 2.574
4 | .729 | 2.282
5 | .577 | 2.115
6 | .483 | 2.004
7 | .419 | 1.924
8 | .373 | 1.864
9 | .337 | 1.816
10 | .308 | 1.777
12 | .266 | 1.716
For x-Charts when we don't know s

## Slide 66: Control Charts for Variables
7 Quality Tools (SPC)
Example
UCL = 12.144
Mean = 12
LCL = 11.856
For x-Charts when we don't know s

## Slide 67: Control Charts for Variables
R – Chart
7 Quality Tools (SPC)
Example
= 2.115*0.25 =
= 0.00*0.25
0.52875
=0
UCL = 0.5287
Mean = 0.25
LCL = 0
For x-Charts when we don't know s

## Slide 68
7 Quality Tools (SPC)
Control Chart for Attributes Data
.

## Slide 69: Control Chart for Attributes Data
SPC
A unit of work is nonconforming (defect or error) or not.
If a unit of work may have one or more nonconformances, entire unit becomes nonconformaning.
Attributes chart captures nonconforming as well as number of nonconforming. Sudden shift in process average.
p-charts monitors proportion of nonconforming units
c-charts and u-charts monitor the number of nonconformances per unit

## Slide 70: p-charts (Fraction nonconforming)
SPC
Sample size needs to be large enough
Average
Collect k samples. Let yi represent the number of nonconforming units in sample i, and ni be the size of sample i.
Compute the fraction nonconforming in each sample, pi = yi /ni
Average fraction nonconforming
P-chart with fixed sample size

## Slide 71: p-charts (Fraction nonconforming)
SPC
.
Collect k samples. Let yi represent the number of nonconforming units in sample i, and ni be the size of sample i.
Compute the fraction nonconforming in each sample, pi = yi /ni
Average fraction nonconforming
Compute standard deviation
P-chart with fixed sample size

## Slide 72: p-charts (Fraction nonconforming)
SPC
.
Compute standard deviation
P-chart with fixed sample size

## Slide 73: p-charts (Fraction nonconforming)
SPC
.
Chart: p-chart
Fraction nonconforming | 0.03 | 0.01 | 0 | 0 | 0.02 | 0.05 | 0.03 | 0.06 | 0.01 | 0.04 | 0 | 0.02 | 0.01 | 0.03 | 0.04 | 0.01 | 0.01 | 0.02 | 0.05 | 0.02 | 0.03 | 0.04 | 0.01 | 0 | 0.01
 | 0.022 | 0.022 | 0.022 | 0.022 | 0.022 | 0.022 | 0.022 | 0.022 | 0.022 | 0.022 | 0.022 | 0.022 | 0.022 | 0.022 | 0.022 | 0.022 | 0.022 | 0.022 | 0.022 | 0.022 | 0.022 | 0.022 | 0.022 | 0.022 | 0.022
 | 0.066 | 0.066 | 0.066 | 0.066 | 0.066 | 0.066 | 0.066 | 0.066 | 0.066 | 0.066 | 0.066 | 0.066 | 0.066 | 0.066 | 0.066 | 0.066 | 0.066 | 0.066 | 0.066 | 0.066 | 0.066 | 0.066 | 0.066 | 0.066 | 0.066
 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Decreasing trend represents improvement
Upper trend or value above UCL conveys
need for improvement
P-chart with fixed sample size

## Slide 74: p-charts (Fraction nonconforming)
SPC
.
P-chart with fixed sample size
Sample size = 350

## Slide 75: p-charts (Fraction nonconforming)
SPC
.
P-chart with variable sample size

## Slide 76: p-charts (Fraction nonconforming)
SPC
.
P-chart with variable sample size
Chart: p-chart
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20
CL | 0.09094 | 0.09094 | 0.09094 | 0.09094 | 0.09094 | 0.09094 | 0.09094 | 0.09094 | 0.09094 | 0.09094 | 0.09094 | 0.09094 | 0.09094 | 0.09094 | 0.09094 | 0.09094 | 0.09094 | 0.09094 | 0.09094 | 0.09094
UCL | 0.16463 | 0.15956 | 0.18087 | 0.16903 | 0.18395 | 0.15402 | 0.16 | 0.17068 | 0.17318 | 0.16332 | 0.16384 | 0.15541 | 0.15255 | 0.1585 | 0.16384 | 0.16518 | 0.15419 | 0.15303 | 0.15505 | 0.15913
LCL | 0.017245 | 0.022317 | 0.0010105 | 0.012846 | -0.0020737 | 0.027862 | 0.021879 | 0.011195 | 0.0086968 | 0.018554 | 0.018039 | 0.026468 | 0.029327 | 0.023378 | 0.018039 | 0.016701 | 0.027693 | 0.02885 | 0.026825 | 0.022747
Fraction NC | 0.13139 | 0.12658 | 0.15217 | 0.04918 | 0.12791 | 0.11765 | 0.038462 | 0.076923 | 0.12727 | 0.084507 | 0.057143 | 0.072626 | 0.02551 | 0.092025 | 0.17857 | 0.088889 | 0.086022 | 0.062176 | 0.082873 | 0.1125

## Slide 77: np-charts (Fraction nonconforming)
SPC
.
np-chart with fixed sample size

## Slide 78: np-charts (Fraction nonconforming)
SPC
.
np-chart with fixed sample size
= 1.4668

## Slide 79: np-charts (Fraction nonconforming)
SPC
.
np-chart with fixed sample size

## Slide 80: c-charts for nonconforming
SPC
Collect samples of equal size and count the number of nonconformances
Compute the average number of nonconformances per unit, c-bar
Standard deviation
Control limits

## Slide 81: c-charts for nonconforming
SPC
.

## Slide 82: c-charts for nonconforming
SPC
.

## Slide 83: u-charts for nonconforming
SPC
.
Applies if the samples are of unequal size
Collect samples and count the number of nonconformances
Compute the average number of nonconformances per unit, u-bar
Standard deviation
Control limits

## Slide 84: u-charts for nonconforming
SPC
.

## Slide 85: u-charts for nonconforming
SPC
.

## Slide 86: References.
Managing for Quality and Performance Excellence, Evans, J.R. and William M. Lindsay, W.M., Cengage Learning, India
The Six Sigma Handbook, Tomas Pyzdek and Paul Keller, Fourth edition, McGraw Hill India.
Total Quality Management, Besterfield et al., Revised third edition, Pearson India
The Management and Control of Quality, J. Evans, and W. Lindsay, Third edition, Cengage Learning

## Slide 87: .
Thanks!